DENCO COILS

Start of each coil is at the lower pin number. All wound on 3/8in. formers with dust cores.

RANGE      MAIN WINDING     AERIAL COUPLING         BASE BIAS              FEEDBACK

OUTPUT COUPLING     (GREEN)

PIN NOS.:                                    1-6                               8-9                                    5-7                              3-4

| 5 | 6.5 turns 20 SWG 9mm long. | 2 turns 30 SWG over main winding between turns. | 1.5 turns 30 SWG on top of other two coils. | 4 turns 30 SWG below tuned winding. |
| --- | --- | --- | --- | --- |
| 4 All 30 SWG | 15.5 turns. | 4 turns above main winding. | 2 turns over bottom of main winding. | 8 turns on top of middle of main winding. |
| 3 All 32 or 34 SWG. | 42.5 turns. | 11 turns above main winding. | 4 turns over bottom of main winding. | 20 turns |

OSCILLATOR COILS

MAIN WINDING(PINS 1-6)                      FEEDBACK         TRANSISTOR

DP                            TRANSISTOR          (DP & TRANSISTOR)    (PINS 8-9)

| 5 | 5.5 turns 20 SWG. | 14 turns 30 SWG. | 2 turns 30 SWG over top of main winding. | 2 turns 30 SWG over bottom of main winding. |
| --- | --- | --- | --- | --- |
| 4 All 30 SWG | 14.5 turns. | 14.5 turns. | 4 turns 1/16in. from top of main winding. | 2 turns over bottom of main winding. |
| 3 All 32 or 34 SWG. | 32 turns. | 32 turns. | 7 turns DP. 3 turns Transistor. | 11 turns over bottom of main winding. |

WHITE COILS

RANGE          INDUCTANCE (uH)

| 1 | 150 |
| --- | --- |
| 2 | 66 |
| 3 | 13.6 |
| 4 | 2.22 |
| 5 | 2.85 |