Heavy Duty Avometer Ranges

| Version | Direct Current | Direct Voltage | Alternating Current | Alternating Voltage | Scale Arc Markings at fsd | Resistance | Scale Arc Markings | Sample Meter/ Reference |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Railway Signalling (GWR) | 50mA 500mA 1A 10A | 1V 5V 50V 200V | 50mA 500mA 1A 10A | 1V 5V 50V 200V | 50 10 200 | ×1 ×100 | 0- 500 | 194-448 |
| Railway Signalling (BR) | 75mA 300mA 1.5A 15A | 1.5 3V 15V 75V 150V 750V | 1.5A 15A | 3V 15V 150V 750V | 3 15 75 | ×1 ×100 | 0- 500 | 2134-1276 |
| Early Commercial - Details to be confirmed | 50mA 500mA 1A 10A | 1V 5V 50V 500V | 50mA 500mA 1A 10A | 1V 5V 50V 500V | 5 10 | ×1 ×100 |  | Richard's Radio Photograph |
| Commercial | 10mA 100mA 1A 10A | 10V 25V 250V 1000V | 10mA 100mA 1A 10A | 10V 25V 250V 1000V | 100 250 | ×1 ×100 | 0- 500 | 11212-1175 Catalogues 1950 1951 1952 1967 (Short Form) |