Record players – a guide for newcomers

The forums frequently get asked for advice on record players, often from new members with a new-found interest in the subject. Of course, the forums are happy to help and encourage in order to keep the interest in vintage technology alive for future generations.

However, a number of basic points often need airing in forum threads and these are touched upon herein. The subject is wide and complex and to cover everything would result in a very large book, so this writing is intended only as a relatively brief introductory guide supplementing the website and forums. The deliberate intention is to cover all-electric machines only, meaning acoustic (wind-up) gramophones and acoustic gramophones with an electric pickup are excluded, as are radiograms.

As a foreword before we reach the main part of this guide, record deck component terminology often causes problems for members new to this aspect of vintage equipment. The deck illustrated below has it’s component names shown and/or makes the purpose of each component clear. The deck shown is a BSR UA14 but the layout of fairly typical of autochangers regardless of make. Some decks may vary in layout, for example some had the Overarm mounted on the left, whilst certain Collaro decks lacked the Size Detector, but the illustration is adequate for general reference.

# Dansette

This is perhaps a good point at which to clear up a common myth concerning Dansette record players.

Dansette was just one of many brands but, for one reason or another, many people nowadays erroneously believe “Dansette” is simply another word for “record player”. This is akin to the way people tend to call any vacuum cleaner a “Hoover” or any rigid plastic from a bygone age “Bakelite”. Another often seen statement is “Dansette style”, which is misleading considering most record players of a given era followed similar general styling. Does “Hoover style Electrolux” make sense? No it doesn’t, so neither does “Dansette style record player”.

Dansette’s record players, more than any of their other products, currently command relatively high prices. This is for one reason only – nostalgia. Dansette was, in its day, a brand which was reasonably affordable and was therefore attractive to the younger generation who wanted the latest Beatles, Rolling Stones etc records. A couple of generations on, people are now reliving those nostalgic days and hence the aforementioned current high prices for Dansette machines. Note the use herein of “Current” and “Currently”; as with all antique and collectable items, prices can and do fluctuate over time.

Dansette products were, in the main, technically ‘average’. This means they weren’t top of the range, as it were, but nor were they total rubbish. Probably 5 out of a score of 1 – 10 would be a fair rating. Nevertheless, Dansette products perhaps had one further edge over their competitors, this being that many were attractively styled and with bright colour schemes – red being a popular colour, even today.

# Fidelity

Fidelity was another brand more or less concurrent with the heyday of Dansette, also relatively cheap and aimed at a similar market. Still common today, Fidelity record players haven’t captured the nostalgia market in the same way as Dansette yet they were of equal, if not slightly better, quality. Perhaps the answer lies in the fact that Fidelity didn’t style (many of) their offerings in such a contemporary way as Dansette did. They could be described as ‘functional-looking’ or, in a few cases, decidedly ‘antiquated’, even for their time.

# Philips/Stella

Unless these brands (Stella were essentially rebadged Philips offerings) sport decks such as BSR or Garrard, avoid them. This is especially applicable to the ‘Disc Jockey’ series. These used the infamous AG3016 rocking pickup headshell with two adjacent styli. When discovered today, the cartridge (which is integral with the headshell) is usually a failure. They can still, just, be replaced, but with a modern equivalent which is now rather expensive – currently £35 - £40.

The Disc Jockey came in several variants, both single play and autochanger. The single play version, in particular, can be notoriously awkward to set up for correct – or even acceptable - operation. So unless you enjoy quirks, a challenge, or both, avoid these Philips/Stella machines.

# El Cheapo machines – general

These are too numerous to mention more than one or two specific makes/models but, broadly, this category embraces the small ‘Attache case’, ‘Vanity case’ or ‘Suitcase’ machines.

Often these have a flimsy cabinet, sometimes even made of Rexine-covered stiff card (sometimes even printed paper was used), a single play deck as crude as you could imagine and a ghastly little loudspeaker which is only fit for getting rid of unwanted visitors on a Sunday afternoon quickly. The Regentone Handygram springs to mind here, to give one example, although for all its shortcomings it is quite nicely styled.

Possible advantages of this type of record player, in trying to think of some, are the convenience of storage once the unwanted visitors have gone and their light weight.

Cautiously, one possible exception (just) is the little Fidelity HF42 model. This has a tone control (mercifully), a rigid plastic cabinet which is easy to clean and has no grille cloth to get damaged. If attracted to one of these, beware of the tonearm though as it’s very fragile. The HF42 is among the best of the worst – possibly.

# Better quality machines

Like the el cheapo models, there is also a wide range of the better quality offerings too numerous to mention beyond a few examples.

‘Better quality’ means a good, sturdy cabinet, a decent (for products aimed at the masses) deck such as a Garrard, a good amplifier, a decent sized loudspeaker and comprehensive controls (separate Bass and Treble, for example). There might also be provision for stereo reproduction via an external, add on, ‘speaker/amplifier unit which, it should be mentioned, are not too easy to obtain nowadays.

A few recommended machines which fall into this general category are the Bush SRP series, the Pye Black Box range (with integral multiple loudspeakers) and the Hacker range. The latter, however, tend to be heavy, quite bulky and rather severe-looking but it’s a matter of personal taste.

# Add-on record players

These are not to be confused with ‘conventional’ record players or the add on ‘speaker/amp units mentioned in the previous section.

The “add-on record player” was literally what the name implies – a device to play records via a suitably equiped radio receiver and using the latter’s amplifier and loudspeaker. This is the purpose of the ‘Gram’ position on, usually but not always, the wavechange switch of many valved radio receivers. As will now be clear, this type of record player contains no amplifier and loudspeaker of its own. The whole ensemble was often known as “the poor man’s radiogram”.

Unfortunately the forums have had occasional members new to record players who have, in all innocence, obtained one of these add-on machines only to later realise his/her purchase is useless on its own. Usually, if not always, these ‘add-ons’ are on a par with the el cheapo machines outlined earlier, although much simpler due to the lack of integral amplifying equipment. Often for 78RPM records only in the case of earlier examples, none of these machines (add-on or otherwise) are recommended for playing cherished or valuable records on and certainly not stereo records. More on stereo later.

A point of historical interest concerns the fairly common ‘Plus-a-Gram’ brand of add-on record player. These were the product of Messrs. J & A Margolin, a firm which later became better known as ‘Dansette’.

# Cartridges and styli

For those new to record players, terminology is often a stumbling block. The cartridge is the device fitted into the headshell (of the tonearm or ‘pickup’) which converts mechanical movements from the record track into electrical signals for the amplifier to do its duty with. The stylus is attached to the cartridge (types and fittings vary widely) and is the actual device which contacts with the record track (groove).

For the purposes of the types of record player with which this document is concerned, there are three types of cartridge; crystal, ceramic and magnetic. The latter, however can be discounted herein as it broadly applies to more modern and/or supposedly high-end equipment. The crystal cartridge is now all-but obsolete and is also the most troublesome nowadays. Briefly, the crystals themselves are prone to dampness, which over time causes the crystals to go soft and ultimately turn into a treacle-like mess. This is usually the fate of the Philips AG3016 mentioned earlier.

A very small selection of common cartridges follows. Relevant text, in italics, is below each image or set of images.

Above is illustrated the infamous Philips AG3016 head. On the left can be seen the letters M (for Microgroove) and N (for Normal, ie 78RPM). On the right is the underside view showing, amongst the goo, the styli mounted side by side.

Unfortunately many old record players which turn up these days have spent some considerable time stored away in lofts, sheds and garages. This means they’ve been exposed to extremes of temperature and, often, dampness – the worst case scenario as far as crystal cartridges and other components are concerned. More on other components later in the ‘Acquiring a record player’ section.

The usual course of action regarding failed crystal cartridges is to replace them with ceramic types. Often this is the still-available BSR SC12M/H of SX6 types, although some ingenuity may be required in order to fit them.

Older records were almost invariably mono, later ones and most – if not all – of those available today are stereo. There exists a common misconception that any old cartridge and stylus is fine for playing any record. Not so. A mono record may be played on any machine using a stylus. For stereo records a stereo cartridge and stylus must be used, or a so-called ‘stereo compatible’ cartridge and stylus.

Be aware that just because a record player is fitted with a stereo cartridge and stylus (or stereo compatible), it does not mean the output of the player is stereo. In perhaps 99% of cases the output is mono.

On cartridge/styli (note the plural of ‘stylus’ is ‘styli’ and not ‘stylii’ as is often amusingly quoted) there are commonly two types and these are largely tied up with the mono and stereo/stereo compatible differences. One type is the ‘turnover’ cartridge with which the entire cartridge turns through 180deg to select the 78RPM stylus on one side, or the microgroove (16/33/45RPM) stylus on the other side. The turnover operation is via a small knob on the front of the tonearm and this type of cartridge is almost always, but not exclusively, mono. They are now less easy to replace although a few presumed ‘repro’ examples exist.

The other main cartridge is the fixed position type which makes use of a turnover stylus. These styli have an arm which projects from the underside of the headshell and are flipped over to select the required stylus. Many of these are marked ‘ST’, for example ‘ST12’, ‘ST15’ and so forth; the letters denoting Stereo.

A few other oddities exist but, for the purposes of keeping this as brief as possible, they will not be included here. A small few older cartridges are illustrated below, most of which are nowadays unlikely to be in good working order.

The top picture shows an older BSR X3M crystal cartridge minus stylus, whilst the bottom picture shows a later BSR X5H type. Both have their mounting brackets present. Both are now obsolete although the X5 types frequently turn up fitted to old record players; some may remain just about in reasonable condition but most are now either failed or failing.

Note the ‘turnover’, or ‘flip over’ stylus, the BSR ST8. ‘ST’ denotes Stereo, although the cartridge is actually Mono. This is an example of what ‘Stereo Compatible’ means. Note, too, the ‘78’ marking. As the unit is illustrated from the underside, the LPS stylus is actually the one positioned for use.

The above two pictures show another commonly found type of cartridge, the TC8 ceramic type. The top picture shows the mono variant, with mounting bracket minus the turnover knob. The bottom picture shows a stereo version. Note the three pins, that in the centre being ‘common ground’.

Visible on the stereo cartridge is an arrow with some markings beside it. There are two sets of those, conveniently indicating which stylus to fit on which side. The two outer pins are marked for Left or Right channels. Although ceramic, these cartridges can no longer be relied upon.

As already touched upon,  common replacements are now the BSR SC12M (Medium output), SC12H (High output) and the SX6 types which, in appearance, resemble the older X5 series. As also already touched upon, a small number of turnover cartridges can still be obtained. An internet search will show the sources. A word of warning when buying cartridges, especially if using an SC12 to replace something else. Make sure the mounting bracket comes with it, or the cartridge will be useless.

One final point concerning cartridges. If a cartridge is replaced with a non original type, as is often the case nowadays, bear in mind tracking weight (pressure of stylus on record) may need adjusting. The height, ie the degree of lift during the auto-cycle, of the tonearm may also need adjustment.

As with all relevant aspects, help and advice is available in the forums if need be.

# Stereophonic record players

As will be gathered from the previous section, true ‘stereo’ (to use the common abbreviated name) record players are quite rare. Some, such as the Pye Black Box, have multiple loudspeakers but can only be described as ‘pseudo stereo’ at best. The rather weird Pye Achoic 1005 and its 3807 export version is one of the very few models which can be described as ‘stereo’ in the true sense of the term. Others, such as the Bush SRP series mentioned earlier, become stereo once their add-on amplifier/loudspeaker units are attached.

In more recent years came what is known as the ‘Stereogram’, the offerings of HMV/Marconiphone (EMI) being about the most common. By and large they’re good units but, being built in similar styles to radiograms, they’re more like pieces of furniture and thus are not portable and so are less popular. That said, if you want something stereo and more modern, plus you have the space, they can be picked up very cheaply if not free.

Beyond those points, it is not intended to elaborate on stereograms and radiograms here as they’re beyond the scope of this article.

# Valved or Transistorised

Both types are common. Vintage technology enthusiasts prefer valved equipment for a number of reasons. If, however, you just want a working record player then the type probably doesn’t matter to you.

Transistorised machines are probably the better option for non technical people. This is because they are low voltage beyond the mains transformer, deck motor excepted, and would likely require less electronic component replacement when compared to a valved machine.

Battery or mains/battery machines will be transistorised and one area in which these differ from mains-only machines is the deck motor, which will be a DC ‘can’ type and usually rated at 9V.

# Acquiring a record player

It is possible to acquire restored record players, at a price, either online via the likes of eBay or via one of a very few specialist dealers who may have their own websites as well as trading via eBay etc.

As mentioned in the Cartridge section earlier however, most old record players which turn up nowadays have spent years laid aside out of use and probably stored in less than ideal conditions. This will likely mean a new mains flex is required (Ideally modern double-insulated flex, with a 3A (Max) fuse in the mains plug), some internal rewiring, component (usually capacitors) replacement and cleaning/degreasing/relubrication of the deck mechanism – especially the ‘trip pawl’ on autochangers.

The Vintage Audio forum section contains some excellent threads concerning the aforementioned grease problem, trip pawls and so forth. Virtually all old record players which have been subjected to long periods of disuse and/or lack of maintenance suffer the grease problem. Newcomers should therefore be prepared to deal with the problem, which will entail full or partial strip-down of the deck - a process which initially can appear quite daunting.

Rubber turntable mats are prone to perishing and good, original replacements are no longer easy to come by.

Idler wheels can also cause problems. At this point it might be an idea to point out that the vast majority of vintage record players use idler wheels to transmit drive from motor to turntable. Many newcomers assume there will be a drivebelt – not so insofar as vintage machines are concerned. The idler wheel (AKA ‘Jockey’ wheel) also acts as a ‘clutch and gearbox’ to engage/disengage the drive and to change speed. The mechanism for these purposes is prone to seizure and also the mounting grommets for the motor can and do perish – causing the motor to drop and correct speeds becoming impossible to select. Other idler wheel problems are failure to drive the turntable due to slipping and damage to its rim caused by the mechanism being left idle but ‘in gear’.

On that latter point note that most speed change selectors do not have an ‘Off’ or ‘0’ position. So when stored out of use ensure the ‘Off’ position is selected on the ‘Start/Manual/Auto’ control. Autochangers and most single-play decks automatically shut off at the end of play in any case.

Above is a typical idler wheel. Many of those by BSR and Garrard are similar in appearance but are not interchangeable. Other types can be found according to age and make of deck but, again, that shown is typical (unless it’s a Philips).

Check the deck Transit Screws, there’ll be at least two of them. One is marked on the deck illustration near the beginning of this guide. When the machine is in use, these screws should be screwed in so the deck floats on its suspension. Otherwise if the machine is being transported or stored in a non horizontal position, the screws should be out (that’s screwed out to their maximum extent, not physically removed) to enable the deck to be secured. Check for this when you acquire your record player as failure to set the Transit Screws correctly can cause damage and/or failure of the deck to operate correctly.

As with almost anything, you need to consider why the record player was taken out of use and stored away in that flooded air raid shelter down the garden in the first place. Perhaps the cartridge failed, perhaps it developed another fault or faults. Others have been taken out of use because, for some mysterious reason, the owner decided to put all his/her music collection onto those CD things and then dumped his/her vinyl records onto the doorstep of a charity shop during the dead of night.

The latter means, of course, that there was actually nothing wrong with the record player when it was put into storage. As is touched upon elsewhere however, remember that age, periods of disuse and unideal storage conditions cause faults to develop. If obtaining an old record player with an unknown history, it’s best to assume work will need doing – regardless of whatever yarn the vendor tells you.

This conveniently brings us to the next section.

# Safety reminder

We are all keen to simply plug in our latest acquisition in order to see what goes bang, but this is a bad idea. There is a risk of damage to the equipment as well as risks of electric shock, fire and explosions – yes, that does say “explosions”.

Our website contains much information on safety issues, via links on the Homepage and also in numerous forum threads which can be searched using appropriate keywords. It is therefore not proposed to repeat this information here, but just because this Safety section has come last does not mean it’s of minor importance.

That said, what is worth repeating here is the warning about equipment designed to operate from AC or DC mains. In the case of record players certain faults, or arguably poor design especially in the case of the el cheapo machines, can result in pickup wiring and/or the entire deck becoming live. Again, this is well covered in our website and its forums and the site owner, moderators and membership take no responsibility for any accidents or injuries caused. A disclaimer to that effect is on view at the bottom of the Homepage.

…..and finally

As said at the beginning, this article is intended as a mere introductory guide to the very basics of record players. To that end we hope it has proved useful. As has already been said, our website and its forums contain much information on various brands, components, faults, repairs and restorations. The Vintage Audio section of the forums is the one that’s specific to record player repairs and advice. Within that section can also be found information on the value of radiograms as well as a list of cartridge and stylus suppliers.

In addition to all the above, information on specific makes and models is available, as is the same for specific makes and models of record deck.

_____________________________________